## Slide 1: A Sequence-to-Sequence (Seq2Seq) Network for Estimating the State of Charge of Li-Ion EV Batteries
S. Meikandadevan
124150028
II M.Sc., Data Science
Guided by,
Dr. Manivannan .R
Department of Mathematics,
SASHE.
School of Arts, Sciences, Humanities and Education (SASHE)

## Slide 2: Motivation
Rechargeable energy storage devices, such as Li- Ion batteries(LIB), have become increasingly popular because of their extended life cycle, high energy density, and light-weight construction for a variety of industrial applications, especially Electric Vehicles (EVs).
Despite its high power and energy density, it is vital for a Battery Management System (BMS) to ensure a safe, efficient, and stable operating state in order to decrease overdesign costs and improve battery performance.
Fig 1 : The Importance of LIB
ZBFB - Zinc–Bromine Flow Battery, VRFB - Vanadium Redox Flow Battery, Na-S - Sodium–Sulfur Battery
Chart: Nominal Voltage(V)
| Nominal Voltage(V)
LIB | 4.3
ZBFB | 1.8
VRFB | 1.4
Na-S | 2.08
Lead-acid | 2
Chart: Life Cycle
| Life Cycle
LIB | 10000
ZBFB | 10000
VRFB | 13000
Na-S | 5000
Lead-acid | 1500
Chart: Depth of Discharge(%)
| Depth of discharge(%)
LIB | 95
ZBFB | 100
VRFB | 100
Na-S | 100
Lead-acid | 50
Chart: Round trip Effeciency(%)
| Round trip effeciency
LIB | 96
ZBFB | 70
VRFB | 70
Na-S | 80
Lead-acid | 82

## Slide 3: Specifications of a Lithium-Ion Battery
Battery chemistry and its specifications | LFP | NCA | NMC
Nominal Voltage (V) | 3.3 V | 3.6 V | 3.6 V
Nominal Capacity (Ah) | 1.1 Ah | 3.2 Ah | 3 Ah
Upper Cut-Off Voltage | 3.6 V | 4.2 V | 4.2 V
Lower Cut-Off Voltage | 2.0 V | 2.5 V | 2.0 V
Temperature (Deg C) | -30 to 60 ˚C | 0 to 45 ˚C | -5 to 50 ˚C
Nominal Mass (g) | 39 g | 48.5 g | 47 g
Table 1 : Different types of LIB
LFP - Lithium Iron Phosphate | NCA - Lithium Nickel Cobalt Aluminium Oxide | NMC - Lithium Nickel Manganese Cobalt Oxide

## Slide 4
Thermal State
(Intermediate)
Aging State
(Large)
Electrical State
(Small)
SOT
SOH
RUL
SOC
SOP/SOF
SOE
Battery Parameters
Capacity
Constraint
Quantitative Relationship
Integration
Temperature
Battery Parameters
Temperature
Heat
Generation
Operating Conditions
The Relationships between various Battery States
Timescales – Small, Large & Intermediate
SOC – State-of-Charge
SOP/SOF – State-of-Power/ State-of-Function
SOE – State-of-Energy
SOH – State-of-Health
RUL – Remaining Useful Lifetime
Fig 2 : Battery States

## Slide 5
Problem Statement
Our objective is to estimate and predict the SOC of the A123 18650 LIB and to achieve more reliability than existing methods comparatively.
To develop an Graphical User Interface(GUI) for predicting the SOC with respect to voltage, current and temperature.
Fig 3 : State-of-Charge

## Slide 6: Various Models Proposed in the Literature
A Data Driven Model is an approach that relies on analyzing large amount of data to make informed decisions and prediction.
Why Data Driven Model ?
Historic Data
Algorithm
Data Driven Insights
Electrical Equivalent Circuit Model
Electrochemical Impendence Model
Data Driven Model
Electro Thermal Model
Fig 4 : Literature Models
Fig 5 : Data Driven Model workflow

## Slide 7
Data Driven Model
Data Driven SOC Estimation Methods
Classification & Regression
Support Vector Machine
Random Forecast
Fuzzy Rule Based
Adaptive Neuro Fuzzy Inference System
Fuzzy Logic
Probabilistic
Gaussian Process Regression
Deep Belief Network
Recurrent Neural Network
Non Linear Autoregression Exogenous Inputs
Long Short Term Memory
Gated Recurrent Unit
Feed Forward Neural Network
Back Propagation Neural Networks
Radial Bias Function Neural Network
Extreme Learning Machines
Wavelet Neural Networks
Deep Feed Forward Neural Networks
Hybrid Algorithms
Hybrid Optimization Based Algorithm
Hybrid Deep Learning Algorithm
Genetic Algorithm
Feed Forward Long Short Term Memory
Fig 6 : D-D Models for SOC estimation available in the literature

## Slide 8
Paper Title | Authors | Algorithms/ Methods | Metrics | Year | Journal Name
A multi-variable multi-step Seq2seq networks for the state of charge estimation of lithium-ion battery [1] | Yufeng Huang , Jian Sun , Lei Xu | LSTM based Seq2Seq [1] | RMSE,MAE,MAPE | 2023 | Case Studies in Thermal Engineering
State-of-charge estimation for lithium-ion batteries based on attentional sequence-to-sequence architecture [2] | Yong Tian , Rucong Lai , Xiaoyu Li , Jindong Tian | LSTM based Seq2Seq [2] | RMSE,MAE | 2023 | Journal of Energy Storage
State-of-Charge Estimation of Lithium-Ion Batteries via Long Short-Term Memory Network [3] | Fangfang Yang, Xiangbao Song, Fan Xu, Kwok-Leung Tsui | LSTM [3] | RMSE,MAE | 2019 | IEEE Xplore
A Comparative Study on Open Circuit Voltage Models for Lithium-ion Batteries [4] | Quan‑Qing Yu1 , Rui Xiong1, Le‑Yi Wang2 and Cheng Lin | Low-Current OCV Test, MATLAB curve fitting toolbox [4] | RMSE | 2018 | Chinese Journal of Mechanical Engineering
A review of machine learning state-of-charge and state-of-health estimation algorithms for lithium-ion batteries [5] | Zhong Ren, Changqing Du | Machine learning & Deep learning algorithms [5] | RMSE,MAE,MAPE | 2023 | Energy Reports
Literature Survey
Table 2 : Literature Survey [1-5]

## Slide 9
PAPER TITLE : A multi-variable multi-step Seq2seq networks for the state of charge estimation of lithium-ion battery.
AUTHORS : Yufeng Huang , Jian Sun , Lei Xu.
JOURNAL NAME : Case Studies in Thermal Engineering.
PUBLICATION YEAR : 2023.
ABSTRACT AND INDEXING : Science Citation Index Expanded, Web of Science, Directory of Open Access Journals (DOAJ), INSPEC.
IMPACT FACTOR : 6.8
CITE SCORE : 7.2
About the Base Paper

## Slide 10
Temperature Profile
Fig 8 : Indian Temperature Map
Fig 7 : World Annual Temperature Map

## Slide 11: Dataset Description
The data set was provided by the Center for Advanced Life Cycle Engineering (CALCE).
Li-ion A123-18650 battery is run through two different profiles (low current and dynamic) at temperatures ranging from 0°C to 50°C with an interval of 10°C.
Subjects | Values (units)
Battery Name | A123 - 18650
Battery Chemistry | LiFePO4
Capacity | 1100 mAh
Voltage (Fully Charged) | 3.6V
Voltage (Cut Off) | 2.4V
Table 3 : A123 LIB Description

## Slide 12
Work Flow
Fig 9 : Work Flow Diagram

## Slide 13: SOC Estimation
A123 Raw Dataset – 30deg Profile
Test_Time(s) | Step_Time(s) | Step_Index | Current(A) | Voltage(V) | Temperature (C)_1
3.004871 | 3.004871 | 1 | 0 | 3.0754 | 31.3912
8.011347 | 5.006164 | 2 | -1.09937 | 2.88858 | 31.24237
13.01757 | 10.01239 | 2 | -1.09937 | 2.876269 | 31.3912
18.02383 | 15.01865 | 2 | -1.09937 | 2.864882 | 31.42165
23.028 | 20.02282 | 2 | -1.09937 | 2.853494 | 31.49606
SOC Estimation
Open Circuit Voltage Method
Reference
SOC
Fig 10 : Flow of SOC estimation
Table 4 : A123 30deg Dataset

## Slide 14: SOC Estimation Cont.,
Using the input parameters such as voltage measured, current measured, and internal resistance, the reference SOC has been estimated.
OCV is the true “electro chemical” indicator of SOC. Estimating OCV is equivalent to estimating SOC. [4]
Fig 11 : OCV - SOC Estimation

## Slide 15
Current | Voltage | Temperature | SOC
1.099941 | 2.82641 | 31.87122 | 36
1.100317 | 2.879962 | 31.82728 | 41
1.099941 | 2.921204 | 31.82728 | 44
1.100129 | 2.955368 | 31.82728 | 47
1.100129 | 2.984606 | 31.78333 | 50
SOC
Current
Temperature
Voltage
A123 Pre-processed Dataset – 30deg Profile
A123-18650 Li-ion battery is run through two different profiles (low current and dynamic) at 30°C temperature.
Input Features
Target Feature
Table 5 : A123 LIB Dataset
Fig 12 : Input & Target Feature

## Slide 16
Sequence-to-Sequence (Seq2Seq) Network
A sequence-to-sequence network can be applied to state of charge (SOC) estimation by taking a sequence of past input values as (encoder), encoding them into a fixed-size context vector, and then decoding this vector into a sequence of future SOC values (decoder).
This allows the model to capture temporal dependencies and predict future SOC values based on historical data, which is essential for accurate SOC estimation in applications such as battery management systems.
Input
Output

## Slide 17
Sequence to Sequence Architecture
Encoder: Compresses input data into a latent space representation using a Multilayer Perceptron (MLP) architecture. Consists of densely connected layers with 16, 32, and 64 neurons, each utilizing the hyperbolic tangent (tanh) activation function. Ends with a Flatten layer to convert the output into a 1D array.
Context Vector: The compressed representation learned by the encoder is repeated and serves as the input for the decoder.
Decoder: Reconstructs the original input from the context vector. Composed of three Gated Recurrent Unit (GRU) layers with 64, 32, and 16 units, respectively. Each GRU layer uses the sigmoid activation function. The final Time Distributed layer with a Dense layer having 1 neuron and a linear activation function outputs the SOC.
GRU
MLP
Inputs
Seq2Seq Network
Target
Current Voltage Temperature
State-of-Charge
Encoder
Decoder

## Slide 18
Advantages over Base paper Model
Efficient Parallelism: Using an MLP for encoding in state-of-charge prediction enables parallel computations, speeding up processing for real-time predictions and scalability.
Generalization with Reduced Overfitting: GRU-based decoding enhances feature extraction while reducing overfitting risks, ensuring accurate predictions across diverse battery conditions.
Compact and Streamlined: The combination of MLP and GRU architectures creates a compact model suitable for onboard battery management, optimizing resource utilization for deployment in electric vehicles and portable devices.
Long/Short Term Memory (LSTM)
Gated Recurrent Unit (GRU)
Input Hidden Layers Output
Input Hidden Layers Output
- Cell memory - Gated memory

## Slide 19
Results and Discussion
Sequence to Sequence Model (%) |  |  |  |  | 
Metrics | N10deg | 10deg | 25deg | 30deg | 40deg
MSE | 0.1139 | 0.0847 | 0.0889 | 0.0880 | 0.0877
RMSE | 0.3375 | 0.2911 | 0.2982 | 0.2967 | 0.2961
MAE | 0.2783 | 0.2512 | 0.2549 | 0.2547 | 0.2528
MAPE | 0.8687 | 0.4859 | 0.4567 | 0.4735 | 0.4492
Metrics like MSE, RMSE, MAE, and MAPE offer quantitative measures to assess model performance. Lower values indicate better accuracy for MSE, RMSE, and MAE, while MAPE provides a percentage-based perspective on prediction errors. Analyzing these metrics collectively helps gauge the model's effectiveness and identify areas for enhancement.
Comparison of Performance Metrics of the Proposed Model
Chart: Seq2seq model results
| N10deg | 10deg | 25deg | 30deg | 40deg
MSE | 0.1139 | 0.0847 | 0.0889 | 0.088 | 0.1024
RMSE | 0.3375 | 0.2911 | 0.2982 | 0.2967 | 0.32
MAE | 0.2783 | 0.2512 | 0.2549 | 0.2547 | 0.265
MAPE | 0.8687 | 0.4859 | 0.4567 | 0.4735 | 0.463
Table 6
Fig 13

## Slide 20
Results and Discussion
Fig 14 : Results Comparison with Base Paper
Chart: N10deg Comparison
| MSE | RMSE | MAE | MAPE
Base Paper | 1.06 | 1.03 | 0.51 | 3.89
Ours | 0.1139 | 0.3375 | 0.2783 | 0.8687
Chart: 10deg Comparison
| MSE | RMSE | MAE | MAPE
Base Paper | 0.2025 | 0.45 | 0.3 | 1.11
Ours | 0.0847 | 0.2911 | 0.2512 | 0.4859
Chart: 25deg Comparison
| MSE | RMSE | MAE | MAPE
Base Paper | 1 | 1 | 0.58 | 3.6
Ours | 0.0889 | 0.2982 | 0.2549 | 0.4567
Chart: 40deg Comparison
| MSE | RMSE | MAE | MAPE
Base Paper | 1.8496 | 1.36 | 0.87 | 5.34
Ours | 0.1024 | 0.32 | 0.265 | 0.463

## Slide 21
Conclusion
In conclusion, our state-of-charge (SOC) prediction model, employing a Multilayer Perceptron (MLP) for encoding and Gated Recurrent Unit (GRU) for decoding, stands out for its efficient parallel processing and enhanced feature extraction capabilities.
Furthermore, we've implemented a user-friendly SOC prediction system using Tkinter, ensuring accurate forecasts for various battery conditions. With its robust architecture and user-friendly interface, our model promises to drive innovation in battery management and contribute to the advancement of energy-efficient technologies.
Chart: Computational Time (Mins)
| N10deg | 10deg | 25deg | 30deg | 40deg
CT (Mins) | 3.6 | 4.6 | 5.3 | 5.23 | 5.1
Fig 16 : Training CT (Mins)
Fig 15 : Residual Plot of 30deg

## Slide 22
Model Deployment
Fig 17 : Model Deployment

## Slide 23: Workplan
Domain & Base paper selection
Literature Survey
Dataset Collection
Data Driven Model Building
Evaluating the Model
GUI & Report Generating
Project Completion
1-Jan-2024
15-Jan-2024
1-Feb-2024
20-Feb-2024
15-Mar-2024
20-Mar-2024
20-Apr-2024

## Slide 24
[1] Y. Huang, J. Sun, L. Xu, "A multi-variable multi-step Seq2seq network for the state of charge estimation of lithium-ion battery," Case Studies in Thermal Engineering, vol. 51, pp. 103566, November 2023. https://doi.org/10.1016/j.csite.2023.103566.
[2] Y. Tian, R. Lai, X. Li, J. Tian, "State-of-charge estimation for lithium-ion batteries based on attentional sequence-to-sequence architecture," Journal of Energy Storage, vol. 62, pp. 106836, June 2023. https://doi.org/10.1016/j.est.2023.106836.
[3] F. Yang, X. Song, F. Xu, and K.-L. Tsui, "State-of-Charge Estimation of Lithium-Ion Batteries via Long Short-Term Memory Network," IEEE ,vol.7,pp.53792-53799,2019. https://doi.org/10.1109/ACCESS.2019.2912803.
[4] Quan‑Qing Yu1, Rui Xiong1, Le‑Yi Wang2 and Cheng Lin, “A Comparative Study on Open Circuit Voltage Models for Lithium-ion Batteries,” Chinese Journal of Mechanical Engineering, pp.31-65,2018.
https://doi.org/10.1186/s10033-018-0268-8.
[5] Zhong Ren, Changqing Du, “A review of machine learning state-of-charge and state-of-health estimation algorithms for lithium-ion batteries,” Energy Reports, vol.9,pp.2993-3021,2023.
https://doi.org/10.1016/j.egyr.2023.01.108.
References

## Slide 25: Thank You